## Slide 1
PPM
A modulation technique for high speed wireless systems
by Jan Boer, Lucent Technologies
November 1997 Doc: IEEE P802.11-97/124
November 1997 Doc: IEEE P802.11-97/124
November 1997 Doc: IEEE P802.11-97/124
November 1997 Doc: IEEE P802.11-97/124
November 1997 Doc: IEEE P802.11-97/124
November 1997 Doc: IEEE P802.11-97/124
November 1997 Doc: IEEE P802.11-97/124

## Slide 2
NOTICE
This document has been prepared by Lucent Technologies Nederland B.V. (“Lucent”) to assist the Standards Working Group IEEE P802.11. It is proposed to the Working Group as a basis for discussion and is not to be construed as a binding proposal on Lucent. Lucent specifically reserves the right to amend or modify the material contained herein and nothing herein shall be construed as conferring or offering licenses or rights with respect to any intellectual property of Lucent.

## Slide 3
Goals for higher speed in ISM band
Raw bitrate 8-10 Mbit/s
Comply to FCC rules
  10 dB processing gain (in case of Direct Sequence)

## Slide 4
Performance criteria
Coverage
  Not more than 10 dB sensitivity drop compared to 802.11
Delay spread
  office 50 ns
  retail up to 200 ns
  industrial > 200 ns

## Slide 5
Compatibility goals
interoperable / coexistence with current 802.11

## Slide 6
What is PPM
PPM is Puls Position Modulation based on the current Direct Sequence technology using the 11-chip Barker Sequence.
Occupying same bandwidth PPM makes high speed possible:
  5, 8, 10 or 11 Mbit/s
Developed at Bell Labs

## Slide 7
Current 802.11 2 Mbit/s system
chip numbers
1
2
3
4
5
6
7
8
9
10
11
symbol
x
x
x
x
x
+11
-11
x
possible
symbol
positions
echoes
Information Rate = 1 bit/symbol/quadrature component = 2 bits/symbol
Chips: 11 (essentially) orthogonal positions due to Barker code
Note: only a single position (out of the 11) is used

## Slide 8
Use 8 out of 11 positions
1
2
3
4
5
6
7
8
9
10
11
symbol
possible
symbol
positions
Chosen
symbol
position
Example: Number of positions, M = 8
K = log M = 3 bits/symbol
2

## Slide 9
Barker Code Pulse Position Modulation
Barker Code
Barker Code
s(t)
s(t -t)
c(t)
+
Matched Filter
to Barker Code
Worst-case correlation
sidelobes can triple, but can
be treated with “Sequence
Estimation” techniques
Distance, d, decreases from
11:1 to 9:3
t
d

## Slide 10
PPM Principals
1
2
3
M
1
2
3
M
M ways to choose each (I&Q)channel
P polarities per channel choice
Number of possible configurations:
N= M*M*P*P
M = 8, P=2 N=256; 8 bits/symbol
M ways to choose both I&Q channels
4 polarities.
N= M *4 = 8*4 = 32 -->5 bits/symbol
Disjoint Quadrature PPM
Joint Quarternary PPM

## Slide 11
Absolute time reference
Possible start positions
of barker sequence
1
2
3
4
5
6
7
8
9
10
11
1
2
3
4
5
6
7
8
9
10
11
1
2
3
4
5
6
7
8
9
10
11
. . . . . . . .
. . . . . . . .
. . . . . . . .
Barker symbol 1
Barker symbol 2
Barker symbol 3
8 Mbps
1
2
3
How to increase datarate
* 3 positions not used by ppm

## Slide 12
10 Mbit/s
Possible start positions
of barker sequence
1
2
3
4
5
6
7
8
9
10
11
1
2
3
4
5
6
7
8
9
10
11
1
2
3
4
5
6
7
8
9
10
11
. . . . . . . .
. . . . . . . .
. . . . . . . .
Barker symbol 1
Barker symbol 2
Barker symbol 3
1
2
3
.818 micro second
symbol time

## Slide 13
11 Mbit/s
Possible start positions
of barker sequence
1
2
3
4
5
6
7
8
9
10
11
1
2
3
4
5
6
7
8
9
10
11
1
2
3
4
5
6
7
8
9
10
11
. . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . . . . . . . .
Barker symbol 1
Barker symbol 2
Barker symbol 3
1
2
3
symbol time
.727 micro second
Barker symbol 4
4
1
2
3
4
5

## Slide 14
Problem with dispersive channel
ICI : Interchip Interference (cross rail)
ISI: Intersymbol Interference
Sequence EstimationTechniques still appropriate
1
2
3
4
5
6
7
8
9
10
11

## Slide 15
Optimum MLSE Reciever
Derivation of Optimum Receiver in
      Barker Code Position Modulation for High-Rate Communication in the ISM Band
Israel Bar David and Rajeev Krishnamoorty
Bell Labs Technical Journal, Autumn 1996
Function to compensate Cross Rail Interference, Side Lobes, ISI
PPM makes reduction of complexity possible at moderate costs

## Slide 16
Receiver complexity
RF and IF
stages
Complete
Mixer
A/D
Correlator
Correlator
LO
Synchronization
andTiming
CPE
CMF
I
Q
Tentative Symbol
Estimator
Mode Sifter
(Viterbi)
Final
Estimates
Conventional Receiver
CPE channel parameter estimator
CMF channel matched filter

## Slide 17
Receiver Functions: Channel Matched Filter
  Concentrate all energy
  Gives optimal sample timing
  Estimation of the channel parameters needed
    many well-known methods
    can be achieved during training
      on preamble

## Slide 18
Receiver Functions: Tentative Symbol Estimator
  With knowledge of channel TSE removes cross rail interference for all possible symbols (actually 256, in essense 64 because polarity is not contributing to complexity)
  Due to autocorrelation properties of Barker sidelobes can initially be ignored (mode sifter can take care)
  Estimates N most likely symbols (N=4)

## Slide 19
Receiver Functions: Mode Sifter
Reduced state trellis structure sifting the tentatively retained modes (maxima of TSE)
Calculates path metric taking ISI and sidelobs into account
Trellis path determines final estimate
  path depth of 4 is sufficient

## Slide 20
Reduced complexity receiver
Implementation specific
Manufactorer choice
At the cost of some performance
Gatecount in order of 2-3 times current 802.11

## Slide 21
Performance
Parameters
  Packet error rate
    100 bytes packets
  SNR
  Time delay spread
    0, 50, 100, 200 ns

## Slide 22
Performance of 8 Mbit/s
Moderate complexity
receiver:
CMF, TSE and MS

## Slide 23
Performance of
8 Mbit/s
Low complexity
receiver (CMF only)

## Slide 24
PPM Performance
SNR

## Slide 25
Performance Highlights
For 5 and 8 Mbit/s a delayspread of 200ns is no problem for a reduced complexity Rx
8 Mbit/s with simple Rx (CMF only) will tolerate 50-70 ns (at FER 10-1)
5 Mbit/s with simple RX can handle at least 100ns
10 and 11Mbit/s can handle 100 ns (at FER 10-1)

## Slide 26
Sensitivity
5 Mbit/s PPM looses compared to 2 Mbit/s 802.11 only 0.5dB
8 Mbit/s PPM 3.5dB
10, 11 Mbit/s in same order as 8 Mbit/s

## Slide 27
PPM and FCC
8 Mbit/s approved by FCC
10/11 there is a risk (increasing symbol rate)
Higher rate in PPM is also possible using QAM (16 QAM gives 10 Mbit/s)
QAM is certainly acceptable by the FCC (performance penalty)

## Slide 28
Comparison to Walsh Code Modulation
Performed same simulation with Harris Walsh code proposal
BER and FER was simulated for framelength 100 bytes
Low complexity receiver, perfect timing and phase sync assumed.

## Slide 29
Performance of Walsh code (Harris proposal)

## Slide 30
Can Walsh be made more robust?
Delayspread above 30 ns (10% FER) is problem
Equalizer---> very complex, less performance (noise enhancement)
maximum likelyhood sequence estimation techniques simular to ppm?
  can not split MLSE into 2 components (TSE and Mode sifter) due to large cross correlations of all Walsh codes
  Walsh sidelobs are high, can not be ignored in TSE to get moderate complexity

## Slide 31
Finally Walsh has compliance issue with FCC
Meets jammer test
Does not meet the ‘required’ spreading code of 10 chips

## Slide 32
Preamble
PPM is Barker sequence based and can train on 802.11 DS preamble (192 microseconds)
Shorter preamble is possible.
  24 microseconds for Rx training (synchronization, channel matched filter)
  + time for energy detection and possibly antenna diversity
  + time to send over header info at higer rate
  total preamble time needed in the order of 50 microseconds

## Slide 33
Coexistence and interoperability issues
With long 802.11 header PPM is fully coexistence and interoperable (can fall back to 1 and 2 Mbit/s)
If 20 micros slottime is maintained also with a short header coexistence and/or interoperability is possible

## Slide 34
Possible coexistence scenario
mix 1/2 Mbit/s with long preamble and PPM with short preamble
  1/2 Mbit detects short preamble (carrier)
    waits for SFD; not found
    defers until energy or carrier drop
  PPM can detect long preamble
long/short can be made to defer for eachother

## Slide 35
Possible interoperability scenario
PPM with both short and long header
  receiver has to detect short or long (short header different from scrambled ones)
In high speed network run short header
falls back to long header if appropriate

## Slide 36
Conclusion
PPM the way to go for higher speed in ISM band
5,8,10,11 Mbit/s
high performance with moderate complexity receiver
receiver complexity implementers choice
FCC approved

## Slide 37
Conclusion con’t
Works fine with IEEE802.11 preamble
  standardization effort minimal, just adds an annex
PPM is not dependent on current IEEE preamble
  througput increase by defining short preamble
  interoperability and coexistence possible